| OPERATORS DAILY INSPECTION RECORD CAR, VAN, BUS | √ = OK N/A = Not Applicable D = Defect | Driver’s Name: |
| --- | --- | --- |
| Name of Company: | Period from: / / To: / / |
| Type of Equipment: | Equipment Model & I.D. No.: |
|  | Mon | Tue | Wed | Thu | Fri | Sat | Sun |
| Headlights (High / Low Beam) |  |  |  |  |  |  |  |
| Tail Lights & Break lights |  |  |  |  |  |  |  |
| Left - right signal lights & Backup lights |  |  |  |  |  |  |  |
| Horn & Backup alarm |  |  |  |  |  |  |  |
| Seatbelts all passengers |  |  |  |  |  |  |  |
| Foot break |  |  |  |  |  |  |  |
| Hand break / parking break |  |  |  |  |  |  |  |
| Rear view mirrors |  |  |  |  |  |  |  |
| Steering system / Power steering level |  |  |  |  |  |  |  |
| Windshield wiper |  |  |  |  |  |  |  |
| Radiator water or coolant leaks / level |  |  |  |  |  |  |  |
| Fuel leaks / level |  |  |  |  |  |  |  |
| Exhaust leaks |  |  |  |  |  |  |  |
| Engine oil leaks / level |  |  |  |  |  |  |  |
| Fan / Alternator belts |  |  |  |  |  |  |  |
| Gear / transmission |  |  |  |  |  |  |  |
| Condition of tires & spare tires |  |  |  |  |  |  |  |
| Instruments / meters |  |  |  |  |  |  |  |
| Windshield & other glasses |  |  |  |  |  |  |  |
| Windows open / close |  |  |  |  |  |  |  |
| Doors open / close |  |  |  |  |  |  |  |
| Condition of body |  |  |  |  |  |  |  |
| Fire extinguisher |  |  |  |  |  |  |  |
| Tools & Jack |  |  |  |  |  |  |  |
| First-aid kit |  |  |  |  |  |  |  |
| Air conditioner |  |  |  |  |  |  |  |
| Radio Connection |  |  |  |  |  |  |  |
| Others |  |  |  |  |  |  |  |
| Driver’s initial |  |  |  |  |  |  |  |
| Remarks |  |
| Any piece of equipment not coming up to the required standards of the Project will not be allowed on / removed / off the project until the necessary repairs have been carried out to the equipment. |
| Verified By: | Signature: | Date: |

| OPERATORS DAILY INSPECTION RECORD FORK LIFT | √ = OK N/A = Not Applicable D = Defect | Driver’s Name: |
| --- | --- | --- |
| Name of Company: | Period from: / / To: / / |
| Type of Equipment: | Equipment Model & I.D. No.: |
|  | Mon | Tue | Wed | Thu | Fri | Sat | Sun |
| Seat, seatbelt |  |  |  |  |  |  |  |
| Windshield, washer |  |  |  |  |  |  |  |
| Windshield wiper |  |  |  |  |  |  |  |
| Rear view mirrors |  |  |  |  |  |  |  |
| Headlights, high/low |  |  |  |  |  |  |  |
| Signal lights |  |  |  |  |  |  |  |
| Tail lights / brake lights |  |  |  |  |  |  |  |
| Horn, back up alarm |  |  |  |  |  |  |  |
| Back up lights |  |  |  |  |  |  |  |
| Engine oil leaks |  |  |  |  |  |  |  |
| Coolant leaks |  |  |  |  |  |  |  |
| Fuel leaks |  |  |  |  |  |  |  |
| Exhaust leaks |  |  |  |  |  |  |  |
| Transmission Controls |  |  |  |  |  |  |  |
| Inching pedal control |  |  |  |  |  |  |  |
| Transmission |  |  |  |  |  |  |  |
| Drive axle |  |  |  |  |  |  |  |
| Steering hydraulics |  |  |  |  |  |  |  |
| Steering cylinders/leaks |  |  |  |  |  |  |  |
| Steering linkage |  |  |  |  |  |  |  |
| Brakes / operation |  |  |  |  |  |  |  |
| Park brake |  |  |  |  |  |  |  |
| Front axle center pin |  |  |  |  |  |  |  |
| Hydraulic pump |  |  |  |  |  |  |  |
| Control valves |  |  |  |  |  |  |  |
| Lift cylinders |  |  |  |  |  |  |  |
| Side shift cylinders |  |  |  |  |  |  |  |
| Mast assembly mounting |  |  |  |  |  |  |  |
| Lift chains / rollers |  |  |  |  |  |  |  |
| Load chart |  |  |  |  |  |  |  |
| Tires, cuts, flat, worn |  |  |  |  |  |  |  |
| Rims, locks, nuts |  |  |  |  |  |  |  |
| Fire extinguisher |  |  |  |  |  |  |  |
| Emergency spill kit |  |  |  |  |  |  |  |
| Others |  |  |  |  |  |  |  |
| Driver’s initial |  |  |  |  |  |  |  |
| Remarks |
| Any piece of equipment not coming up to the required standards of the Project will not be allowed on / removed / off the project until the necessary repairs have been carried out to the equipment. |
| Verified by: | Signature: | Date: |

| OPERATORS DAILY INSPECTION RECORD BULL DOZER | √ = OK N/A = Not Applicable D = Defect | Driver’s Name: |
| --- | --- | --- |
| Name of Company: | Period from: / / To: / / |
| Type of Equipment: | Equipment Model & I.D. No.: |
|  | Mon | Tue | Wed | Thu | Fri | Sat | Sun |
| Seat, seatbelt |  |  |  |  |  |  |  |
| Windshield, washer |  |  |  |  |  |  |  |
| Windshield wiper |  |  |  |  |  |  |  |
| Rear view mirrors |  |  |  |  |  |  |  |
| Headlights, high/low |  |  |  |  |  |  |  |
| Signal lights |  |  |  |  |  |  |  |
| Tail lights / brake lights |  |  |  |  |  |  |  |
| Horn, back up alarm |  |  |  |  |  |  |  |
| Back up lights |  |  |  |  |  |  |  |
| Engine oil leaks |  |  |  |  |  |  |  |
| Coolant leaks |  |  |  |  |  |  |  |
| Fuel leaks |  |  |  |  |  |  |  |
| Exhaust leaks |  |  |  |  |  |  |  |
| Transmission Controls |  |  |  |  |  |  |  |
| Torque converter/oil leak |  |  |  |  |  |  |  |
| Master clutch/slippage |  |  |  |  |  |  |  |
| Steering left / right |  |  |  |  |  |  |  |
| Brakes left / right |  |  |  |  |  |  |  |
| Sprockets, bolts, nuts |  |  |  |  |  |  |  |
| Track frames, cracks |  |  |  |  |  |  |  |
| Idlers / Oil Leak |  |  |  |  |  |  |  |
| Rollers / leaks |  |  |  |  |  |  |  |
| Pins, bushings, pad |  |  |  |  |  |  |  |
| Shoes, bolts, nuts |  |  |  |  |  |  |  |
| Hydraulic tank / leaks |  |  |  |  |  |  |  |
| Hydraulic pump |  |  |  |  |  |  |  |
| Control valves |  |  |  |  |  |  |  |
| Lift cylinders |  |  |  |  |  |  |  |
| Blade, cutting edge, ends |  |  |  |  |  |  |  |
| Push arms, cracks, pins |  |  |  |  |  |  |  |
| Ripper mounting bolts |  |  |  |  |  |  |  |
| Fame cracks |  |  |  |  |  |  |  |
| Tooth, pin, lock |  |  |  |  |  |  |  |
| Fire extinguisher |  |  |  |  |  |  |  |
| Emergency spill kit |  |  |  |  |  |  |  |
| Others |  |  |  |  |  |  |  |
| Driver’s initial |  |  |  |  |  |  |  |
| Remarks |
| Any piece of equipment not coming up to the required standards of the Project will not be allowed on / removed / off the project until the necessary repairs have been carried out to the equipment. |
| Verified by: | Signature: | Date: |

| OPERATORS DAILY INSPECTION RECORD DUMP TRUCK / FLAT BED / TANKER | √ = OK N/A = Not Applicable D = Defect | Driver’s Name: |
| --- | --- | --- |
| Name of Company: | Period from: / / To: / / |
| Type of Equipment: | Equipment Model & I.D. No.: |
|  | Mon | Tue | Wed | Thu | Fri | Sat | Sun |
| Step, Door Handle, Latch |  |  |  |  |  |  |  |
| Seat, seat belt |  |  |  |  |  |  |  |
| Windshield, washer |  |  |  |  |  |  |  |
| Windshield wiper |  |  |  |  |  |  |  |
| Rear view mirrors |  |  |  |  |  |  |  |
| Headlights, high/low |  |  |  |  |  |  |  |
| Signal lights |  |  |  |  |  |  |  |
| Tail lights / brake lights |  |  |  |  |  |  |  |
| Horn, back up alarm |  |  |  |  |  |  |  |
| Back up lights |  |  |  |  |  |  |  |
| Engine oil leaks |  |  |  |  |  |  |  |
| Coolant leaks |  |  |  |  |  |  |  |
| Fuel leaks |  |  |  |  |  |  |  |
| Exhaust leaks |  |  |  |  |  |  |  |
| Transmission; Oil Leaks |  |  |  |  |  |  |  |
| Works in all gears |  |  |  |  |  |  |  |
| Power take off Oil leaks |  |  |  |  |  |  |  |
| Rear Axles; Oil leaks |  |  |  |  |  |  |  |
| Cracked Wheel Rims |  |  |  |  |  |  |  |
| Broken /loose wheel nuts |  |  |  |  |  |  |  |
| Steering linkage |  |  |  |  |  |  |  |
| Brakes / leaks |  |  |  |  |  |  |  |
| Brake test |  |  |  |  |  |  |  |
| Suspension springs |  |  |  |  |  |  |  |
| Hydraulic system |  |  |  |  |  |  |  |
| Dump / Tailgate locks |  |  |  |  |  |  |  |
| Dump body frame cracks |  |  |  |  |  |  |  |
| Mud flaps |  |  |  |  |  |  |  |
| Tires |  |  |  |  |  |  |  |
| Mounting nuts / studs |  |  |  |  |  |  |  |
| Spare tire |  |  |  |  |  |  |  |
| Tools and Jack |  |  |  |  |  |  |  |
| Fire extinguisher |  |  |  |  |  |  |  |
| Emergency Spill Kit |  |  |  |  |  |  |  |
| Bonding cable and clamp |  |  |  |  |  |  |  |
| Transfer pump / hose condition |  |  |  |  |  |  |  |
| Hazard signs and symbol |  |  |  |  |  |  |  |
| Tanker cover / vent |  |  |  |  |  |  |  |
| Others |  |  |  |  |  |  |  |
| Driver’s initial |  |  |  |  |  |  |  |
| Remarks |
| Any piece of equipment not coming up to the required standards of the Project will not be allowed on / removed / off the project until the necessary repairs have been carried out to the equipment. |
| Verified by: | Signature: | Date: |

| OPERATORS DAILY INSPECTION RECORD GRADER, WHEEL LOADER and BACKHOE | √ = OK N/A = Not Applicable D = Defect | Driver’s Name: |
| --- | --- | --- |
| Name of Company: | Period from: / / To: / / |
| Type of Equipment: | Equipment Model & I.D. No.: |
|  | Mon | Tue | Wed | Thu | Fri | Sat | Sun |
| Cab, ROPS |  |  |  |  |  |  |  |
| Step, Door Handle, Latch |  |  |  |  |  |  |  |
| Seat, Seatbelt, Cleanliness |  |  |  |  |  |  |  |
| Windshield, Cab Glass |  |  |  |  |  |  |  |
| Windshield Wiper, Washer |  |  |  |  |  |  |  |
| Indicators, Gauges |  |  |  |  |  |  |  |
| Audio, Visual Alarms |  |  |  |  |  |  |  |
| Switches |  |  |  |  |  |  |  |
| Mirrors, Rear, Left, Right |  |  |  |  |  |  |  |
| Headlights, Low / High Beam |  |  |  |  |  |  |  |
| Work lights, front, rear |  |  |  |  |  |  |  |
| Tail Lights, Brake Lights |  |  |  |  |  |  |  |
| Horn |  |  |  |  |  |  |  |
| Electrical System Wiring |  |  |  |  |  |  |  |
| Batteries, Covers, Hold Downs |  |  |  |  |  |  |  |
| Brake Pedal |  |  |  |  |  |  |  |
| Transmission Controls |  |  |  |  |  |  |  |
| Bucket, lift arm controls |  |  |  |  |  |  |  |
| Oil Leaks |  |  |  |  |  |  |  |
| Coolant Leaks |  |  |  |  |  |  |  |
| Fuel Leaks |  |  |  |  |  |  |  |
| Fan, Guards, Belts |  |  |  |  |  |  |  |
| Exhaust System, Leaks, Silencer |  |  |  |  |  |  |  |
| Front axel – spindle, seal, bolts etc. |  |  |  |  |  |  |  |
| Rear axel – spindle, seal, bolts etc. |  |  |  |  |  |  |  |
| Steering linkage |  |  |  |  |  |  |  |
| Breaks / leaks |  |  |  |  |  |  |  |
| Break test |  |  |  |  |  |  |  |
| Hydraulic system |  |  |  |  |  |  |  |
| Compressor / air tank |  |  |  |  |  |  |  |
| Lift arm cracks |  |  |  |  |  |  |  |
| Bucket structure cracks |  |  |  |  |  |  |  |
| Out riggers |  |  |  |  |  |  |  |
| Fire extinguisher |  |  |  |  |  |  |  |
| Emergency spill kit |  |  |  |  |  |  |  |
| Tires condition |  |  |  |  |  |  |  |
| Mounting nuts / studs |  |  |  |  |  |  |  |
| Others |  |  |  |  |  |  |  |
| Driver’s initial |  |  |  |  |  |  |  |
| Remarks |
| Any piece of equipment not coming up to the required standards of the Project will not be allowed on / removed / off the project until the necessary repairs have been carried out to the equipment. |
| Verified by: | Signature: | Date: |

| OPERATORS DAILY INSPECTION RECORD EXCAVATOR | √ = OK N/A = Not Applicable D = Defect | Driver’s Name: |
| --- | --- | --- |
| Name of Company: | Period from: / / To: / / |
| Type of Equipment: | Equipment Model & I.D. No.: |
|  | Mon | Tue | Wed | Thu | Fri | Sat | Sun |
| Cab, ROPS |  |  |  |  |  |  |  |
| Step, Door Handle, Latch |  |  |  |  |  |  |  |
| Seat, Seatbelt, Cleanliness |  |  |  |  |  |  |  |
| Windshield, Cab Glass |  |  |  |  |  |  |  |
| Windshield Wiper, Washer |  |  |  |  |  |  |  |
| Indicators, Gauges |  |  |  |  |  |  |  |
| Switches |  |  |  |  |  |  |  |
| Mirrors, Rear, Left, Right |  |  |  |  |  |  |  |
| Work Lights, Front, Rear |  |  |  |  |  |  |  |
| Horn |  |  |  |  |  |  |  |
| Travel Alarms, forward, reverse |  |  |  |  |  |  |  |
| Electrical System Wiring |  |  |  |  |  |  |  |
| Batteries, Covers, Hold Downs |  |  |  |  |  |  |  |
| Oil Leaks |  |  |  |  |  |  |  |
| Coolant Leaks |  |  |  |  |  |  |  |
| Fuel Leaks |  |  |  |  |  |  |  |
| Fan, Guards, Belts |  |  |  |  |  |  |  |
| Exhaust System, Leaks, Silencer |  |  |  |  |  |  |  |
| Transmission Controls |  |  |  |  |  |  |  |
| Torque converter/oil leak |  |  |  |  |  |  |  |
| Master clutch/slippage |  |  |  |  |  |  |  |
| Steering left / right |  |  |  |  |  |  |  |
| Brakes left / right |  |  |  |  |  |  |  |
| Sprockets, bolts, nuts |  |  |  |  |  |  |  |
| Track frames, cracks |  |  |  |  |  |  |  |
| Idlers / Oil Leak |  |  |  |  |  |  |  |
| Rollers / leaks |  |  |  |  |  |  |  |
| Pins, bushings, pad |  |  |  |  |  |  |  |
| Shoes, bolts, nuts |  |  |  |  |  |  |  |
| Hydraulic tank / leaks |  |  |  |  |  |  |  |
| Hydraulic pump |  |  |  |  |  |  |  |
| Control valves |  |  |  |  |  |  |  |
| Lift cylinders |  |  |  |  |  |  |  |
| Boom & bucket structural cracks |  |  |  |  |  |  |  |
| Pins, locks, bushings |  |  |  |  |  |  |  |
| Swing drive gear case, noise, oil leaks |  |  |  |  |  |  |  |
| Fire extinguisher |  |  |  |  |  |  |  |
| Emergency spill kit |  |  |  |  |  |  |  |
| Others |  |  |  |  |  |  |  |
| Driver’s initial |  |  |  |  |  |  |  |
| Remarks |
| Any piece of equipment not coming up to the required standards of the Project will not be allowed on / removed / off the project until the necessary repairs have been carried out to the equipment. |
| Verified by: | Signature: | Date: |

| OPERATORS DAILY INSPECTION RECORD SOIL COMPACTOR | √ = OK N/A = Not Applicable D = Defect | Driver’s Name: |
| --- | --- | --- |
| Name of Company: | Period from: / / To: / / |
| Type of Equipment: | Equipment Model & I.D. No.: |
|  | Mon | Tue | Wed | Thu | Fri | Sat | Sun |
| Cab, ROPS |  |  |  |  |  |  |  |
| Step, Door Handle, Latch |  |  |  |  |  |  |  |
| Seat, Seatbelt, Cleanliness |  |  |  |  |  |  |  |
| Windshield, Cab Glass |  |  |  |  |  |  |  |
| Windshield Wiper, Washer |  |  |  |  |  |  |  |
| Indicators, Gauges |  |  |  |  |  |  |  |
| Audio, Visual Alarms |  |  |  |  |  |  |  |
| Switches |  |  |  |  |  |  |  |
| Mirrors, Rear, Left, Right |  |  |  |  |  |  |  |
| Headlights, Low / High Beam |  |  |  |  |  |  |  |
| Work lights, front, rear |  |  |  |  |  |  |  |
| Tail Lights, Brake Lights |  |  |  |  |  |  |  |
| Horn |  |  |  |  |  |  |  |
| Electrical System Wiring |  |  |  |  |  |  |  |
| Batteries, Covers, Hold Downs |  |  |  |  |  |  |  |
| Brake Pedal |  |  |  |  |  |  |  |
| Transmission Controls |  |  |  |  |  |  |  |
| Vibrator control |  |  |  |  |  |  |  |
| Steering linkage |  |  |  |  |  |  |  |
| Oil Leaks |  |  |  |  |  |  |  |
| Coolant Leaks |  |  |  |  |  |  |  |
| Fuel Leaks |  |  |  |  |  |  |  |
| Fan, Guards, Belts |  |  |  |  |  |  |  |
| Exhaust System, Leaks, Silencer |  |  |  |  |  |  |  |
| Steering linkage |  |  |  |  |  |  |  |
| Breaks / leaks |  |  |  |  |  |  |  |
| Break test |  |  |  |  |  |  |  |
| Hydraulic system |  |  |  |  |  |  |  |
| Drive axel housing |  |  |  |  |  |  |  |
| Torque Converter, Oil Leaks, Slippage |  |  |  |  |  |  |  |
| Vibrator drum assembly |  |  |  |  |  |  |  |
| Fire extinguisher |  |  |  |  |  |  |  |
| Emergency spill kit |  |  |  |  |  |  |  |
| Tires condition |  |  |  |  |  |  |  |
| Mounting nuts / studs |  |  |  |  |  |  |  |
| Others |  |  |  |  |  |  |  |
| Driver’s initial |  |  |  |  |  |  |  |
| Remarks |
| Any piece of equipment not coming up to the required standards of the Project will not be allowed on / removed / off the project until the necessary repairs have been carried out to the equipment. |
| Verified by: | Signature: | Date: |

| OPERATORS DAILY INSPECTION RECORD TRANSIT MIXTURE / CONCRETE PUMP | √ = OK N/A = Not Applicable D = Defect | Driver’s Name: |
| --- | --- | --- |
| Name of Company: | Period from: / / To: / / |
| Type of Equipment: | Equipment Model & I.D. No.: |
|  | Mon | Tue | Wed | Thu | Fri | Sat | Sun |
| Step, Door Handle, Latch |  |  |  |  |  |  |  |
| Seat, seat belt |  |  |  |  |  |  |  |
| Windshield, washer |  |  |  |  |  |  |  |
| Windshield wiper |  |  |  |  |  |  |  |
| Rear view mirrors |  |  |  |  |  |  |  |
| Headlights, high/low |  |  |  |  |  |  |  |
| Signal lights |  |  |  |  |  |  |  |
| Tail lights / brake lights |  |  |  |  |  |  |  |
| Horn, back up alarm |  |  |  |  |  |  |  |
| Back up lights |  |  |  |  |  |  |  |
| Engine oil leaks |  |  |  |  |  |  |  |
| Coolant leaks |  |  |  |  |  |  |  |
| Fuel leaks |  |  |  |  |  |  |  |
| Exhaust leaks |  |  |  |  |  |  |  |
| Transmission; Oil Leaks |  |  |  |  |  |  |  |
| Works in all gears |  |  |  |  |  |  |  |
| Front & Rear Axles; Oil leaks |  |  |  |  |  |  |  |
| Cracked Wheel Rims |  |  |  |  |  |  |  |
| Broken /loose wheel nuts |  |  |  |  |  |  |  |
| Tires |  |  |  |  |  |  |  |
| Spare tire |  |  |  |  |  |  |  |
| Mud flaps |  |  |  |  |  |  |  |
| Steering linkage |  |  |  |  |  |  |  |
| Brakes / leaks |  |  |  |  |  |  |  |
| Brake test |  |  |  |  |  |  |  |
| Suspension springs |  |  |  |  |  |  |  |
| Hydraulic system |  |  |  |  |  |  |  |
| Drum drive gear box, oil leak |  |  |  |  |  |  |  |
| Drum rear support bearing |  |  |  |  |  |  |  |
| Charging hopper access ladder, hand hold, rails, screen |  |  |  |  |  |  |  |
| Drum drive control |  |  |  |  |  |  |  |
| Water tank, piping, valve, hose |  |  |  |  |  |  |  |
| Pouring arm function |  |  |  |  |  |  |  |
| Remote switches, operation |  |  |  |  |  |  |  |
| Fire extinguisher |  |  |  |  |  |  |  |
| Emergency Spill Kit |  |  |  |  |  |  |  |
| Wheel Choker |  |  |  |  |  |  |  |
| Others: |  |  |  |  |  |  |  |
| Driver’s initial |  |  |  |  |  |  |  |
| Remarks |
| Any piece of equipment not coming up to the required standards of the Project will not be allowed on / removed / off the project until the necessary repairs have been carried out to the equipment. |
| Verified by: | Signature: | Date: |

| OPERATORS DAILY INSPECTION RECORD TRACTOR / TRAILOR | √ = OK N/A = Not Applicable D = Defect | Driver’s Name: |
| --- | --- | --- |
| Name of Company: | Period from: / / To: / / |
| Type of Equipment: | Equipment Model & I.D. No.: |
|  | Mon | Tue | Wed | Thu | Fri | Sat | Sun |
| Cab, ROPS |  |  |  |  |  |  |  |
| Step, Handle |  |  |  |  |  |  |  |
| Seat, seat belt |  |  |  |  |  |  |  |
| Rear view mirrors |  |  |  |  |  |  |  |
| Headlights, high/low |  |  |  |  |  |  |  |
| Signal lights |  |  |  |  |  |  |  |
| Tail lights / brake lights |  |  |  |  |  |  |  |
| Horn, back up alarm |  |  |  |  |  |  |  |
| Back up lights |  |  |  |  |  |  |  |
| Engine oil leaks |  |  |  |  |  |  |  |
| Coolant leaks |  |  |  |  |  |  |  |
| Fuel leaks |  |  |  |  |  |  |  |
| Exhaust leaks |  |  |  |  |  |  |  |
| Transmission; Oil Leaks |  |  |  |  |  |  |  |
| Works in all gears |  |  |  |  |  |  |  |
| Rear Axles; Oil leaks |  |  |  |  |  |  |  |
| Clutch – free play, noise |  |  |  |  |  |  |  |
| Cracked Wheel Rims |  |  |  |  |  |  |  |
| Broken /loose wheel nuts |  |  |  |  |  |  |  |
| Tires |  |  |  |  |  |  |  |
| Batteries – cover, terminals |  |  |  |  |  |  |  |
| Steering linkage |  |  |  |  |  |  |  |
| Brakes / leaks |  |  |  |  |  |  |  |
| Brake test |  |  |  |  |  |  |  |
| Hydraulic system |  |  |  |  |  |  |  |
| Tie rod, mechanical linkage |  |  |  |  |  |  |  |
| Trailer – deck, frame, king pin |  |  |  |  |  |  |  |
| Power take off |  |  |  |  |  |  |  |
| Springs / Hangers / pins / Brackets / U bolts |  |  |  |  |  |  |  |
| Fire extinguisher |  |  |  |  |  |  |  |
| Emergency Spill Kit |  |  |  |  |  |  |  |
| Others: |  |  |  |  |  |  |  |
| Driver’s initial |  |  |  |  |  |  |  |
| Remarks |
| Any piece of equipment not coming up to the required standards of the Project will not be allowed on / removed / off the project until the necessary repairs have been carried out to the equipment. |
| Verified by: | Signature: | Date: |