PERIODIC INSPECTION OF PORTABLE ELEC EQPT

INSPECTION DATE:

FORM NO.:MPT/ELEC/PI/MOT/01/A

| TYPE OF EQPT | Portable motor driven pumps / compressors / heaters |
| --- | --- |
| TAG NO. |  | Rating |  |
| MAKE |  | SL.NO. |  |
| Model No. |  | Single phase / Three phase |  |
| LOCATION OF THE M/C AT THE TIME OF INSPN |  |  |
| APPLICATION |  |  |
| NAME OF THE CONTRACTOR |  |  |
| CONTRACT SUPERVISOR NAME |  |  |
| CONTACT NO. |  |  |

Please fill in the below check list and mention clearly the non-compliance if any in the remarks column. Separate check list for each pump shall be filled.

| S.No. | Checking parameter | OK | NOT OK | Remarks |
| --- | --- | --- | --- | --- |
| 1 | The IR value of the motor / heater |  |  | Minimum IR value should be 5 Meg ohm for motors and 1 Meg ohm for heaters |
| 2 | Power cable is of copper and size Ok as per motor / heater rating |  |  |  |
| 3 | No non-standard power and control cable joints in place |  |  | In case jointing is required it is to be made with proper splicing kit |
| 4 | The Contactor rating OK |  |  |  |
| 5 | The overload relay range is OK |  |  |  |
| 6 | The main I/C or individual feeder has ELR protection |  |  |  |
| 7 | The MCCB / Fuse rating is OK as per motor / heater rating |  |  |  |
| 8 | The control circuit wiring condition |  |  |  |
| 9 | Control circuit protection MCB / Fuse |  |  |  |
| 10 | Cable termination done with proper gland and lugs |  |  |  |
| 11 | Grounding of the motor / heater / base frame |  |  |  |
| 12 | Enclosure of the motor / heater |  |  |  |
| 13 | Motor cooling fan blades and fan cover |  |  |  |
| 14 | Motor terminal box and cover properly placed and all fasteners are tightened |  |  |  |
| 15 | Motor base tightness to the frame |  |  |  |
| 16 | The coupling guard in place |  |  |  |
| 17 | The heater coil has thermostat for temperature control and in operation |  |  |  |
| 18 | The heater coil has level control and gets automatic cutoff in case of level low |  |  |  |
| 19 | Motor / heater name plate details noted down and attached as separate sheet |  |  |  |
| 20 | Motor / heater on line performance checked |  |  |  |
| 21 | The actual current drawn by the motor / heater and is less than the FLC |  |  |  |
| 22 | Motor bearing noise |  |  |  |
| 23 | Overall starter unit condition |  |  |  |
| 24 | In case of single phase maching the condenser is secured properly and not held loosely. |  |  |  |
| 25 | The condenser wiring terminals are soldered properly without loose connection |  |  |  |

The above points shall be checked thoroughly and in case of any critical non – compliance the machine should not be allowed to operate until the points are complied with.

| Overall condition | OK | NOT OK |
| --- | --- | --- |
| Give brief reasons for Not OK: |
| In case of Not OK, ensure the machine is moved away from the process area and the corrective action is being taken. Inform the respective contractor and CEIL department superintendents |

Next Due date for inspection:

Suggested corrective actions:

Inspected by

| Inspected by | Name | Signature |
| --- | --- | --- |
| Elec Engineer |  |  |
| HSE Engineer |  |  |
| Contract representative |  |  |